The classical vibrationally adiabatic potential curve is defined as:
V_a( s ) = ∆ V_MEP( s) + h over 2 sum from{ i=1 }to{ 3N-7 } %omega_i( s )	(1)

being ∆VMEP the potential energy relative to reactants, and ωi the corresponding vibrational frequencies of the geometry s. The corresponding vibrationally adiabatic transmission coefficient can be calculated, under the Wentzel–Kramers–Brillouin (WKB) approximation, as:
%kappa = 1+e^{{V^max_a over {k_B T} }} 1 over {k_B T} int_{0}^{%infinite}{P left( V_a right) e^{-{V_a over {k_B T} }} dV_a}	(2)

where the approximation is valid at low temperatures[1]. The value of the tunneling probability for a given adiabatic potential E is defined by[2]:
[1] Equations 49, 50 from J.Phys.Chem. 1980 (84) 1730-1748
[2] Equations 44, 45 from J.Phys.Chem. 1992 (96) 5758-5772; or 1a from J.Am.Chem.Soc. 2002 (124) 3093-3124
P left( E right) = left( 1 + e^{2 cdot %theta left( E right)} right)^{ {}-1 } ~~~~ E <= V_a^{s=0} ~~~~~~~~ %theta left( E right) = {2 %pi} over h int_{ s<{} }^{ s>{} }{ left(2 %mu_eff (s)left[ V_a left( s right)- E right] right)^{1 over 2} ds }	(3)

where s< and s> are the values of the path coordinate at the left and right turning points (values of the reaction coordinate with a value for the adiabatic potential of E), and %mu_eff( s ) is the effective reduced mass along s. If %mu_eff is taken constant along the reaction path (equal to 1), we obtain the Zero-curvature theory (ZCT). On the other hand, the centrifugal-dominant small-curvature tunneling approximation[3] allows to express the dependence of %mu_eff( s ) :
[3] Equations 44, 50, 51, 52 from Comput. Phys. Commun. 1992 (71) 235-262; and 3 from J.Am.Chem.Soc. 2002 (124) 3093-3124
%mu_eff(s) = %mu cdot min left lbrace e^{- 2 a(s) - left[ a(s) right]^2 + left( {d%tau (s)} over ds right)^2 } ~,~ 1 right rbrace	(4)

where the exponential only is evaluated if the exponent is negative, and a(s) and τ(s) (the maximum concave-side vibrational displacement along the curvature direction) are defined as follows:
a( s ) = %tau( s ) %eta( s ) ~~~~~~ %tau (s) = %eta^{ 1 over 2 }(s) left( h over {2 %pi %mu} right)^{ 1 over 2 } left[ sum from{i} to{3N-7}{ B_i^2(s) %omega_i^2(s)} right]^{ - {1 over 4} } ~~~~~~ %eta (s) = left( sum from{i} to{3N-7}{ B_i^2 (s) } right)^{ 1 over 2 }	(5)

being %eta( s ) the magnitude of the curvature, and B_i( s ) the reaction path curvature components:
B_i ( s ) = 1 over lline g(s) rline L^T_i(s) cdot { left[ H(s) cdot { {-g(s)} over lline g(s) rline } right] }	(6)

In this expression, Li(s) corresponds to the ith eigenvector of the hessian H, and g is the gradient vector (all in mass-weight coordinates: x_i = sqrt{ m_i } x^cart_i ~~;~~ g_i = g^cart_i / sqrt{ m_i } ~~;~~ h_{ i,j } = h^cart_{ i,j } / sqrt{ m_i · m_j } ). Thus, the Bi(s) values represent the change in the direction of the ith eigenvector induced by the variation of the reaction coordinate.

%theta left( x right) = s over { kg m^2 } int_{ s<{} }^{ s>{} }{ left( %mu right)^{1 over 2} sqrt{ 2 kg {m^2 over s^2 } } Å sqrt{ g over mol } } newline %theta left( x right) = left( s over { kg m^2 } int_{ s<{} }^{ s>{} }{ left( %mu right)^{1 over 2} sqrt{kg} {m^2 over s} sqrt{kg} } right) sqrt{2} {10^-10 over sqrt{10^3 · N_A} { {2 · %pi} over h } } newline newline a(s): "dimensionless" ~~;~~ %tau(s): Å sqrt{ g over mol } ~~;~~ %eta(s): 1 over { Å sqrt{ g over mol } } ~~;~~ B_m(s): 1 over { Å sqrt{ g over mol } }
For the particle in a box, the tunneling effect arises from the presence of a finite potential of the shape:
V( x ) left lbrace matrix { 0# x < 0# "region I"## U_o# 0 <= x <= L# "region II"## 0# x > L# "region III"} right none
The Schrödinger time-independent equation is solved for each region, thus obtaining three wave-functions, satisfying the continuity at each region, as well as in the first derivatives:
%psi_I( 0 ) = %psi_II( 0 ) ~~~~ ~~ %psi_II( L ) = %psi_III( L ) ~~~~ ~~ left none { d %psi_I(x) } over { dx } right rline_{ x=0 } = left none { d %psi_II(x) } over { dx } right rline_{ x=0 } ~~~~ ~~ left none { d %psi_II(x) } over { dx } right rline_{ x=L } = left none { d %psi_III(x) } over { dx } right rline_{ x=L }

The transmission coefficient represents the probability flux of the transmitted wave relative to that of the incident wave. Using the WKB approximation[4], one can obtain a tunneling coefficient that looks like (which depends on the particular system):
[4] See chapter 8 of “Introduction to Quantum Mechanics” (ISBN: 0-13-191175-9)
T ={ e^{ -2 int_{x1}^{x2}{ sqrt{ {2 m} over { %Ux210F^2} left( V(x) -E right) } dx } } } over { left( 1 + 1 over 4 e^{ -2 int_{x1}^{x2}{ sqrt{ {2 m} over { %Ux210F^2} left( V(x) -E right) } dx } } right)^2 }
where x1, x2 are the two classical turning points for the potential barrier.

A description of the Variational Transition-State theory can be found at J.Phys.Chem. 1980 (84) 1730-1748
See also J.Am.Chem.Soc. 1993 (115) 2408-2415 for SCT.