The classical vibrationally adiabatic potential curve is defined as:
V_a( s ) = V_MEP( s) + h over 2 sum from{ i=1 }to{ 3N-7 } %omega_i( s )	(1)

being ωi the corresponding vibrational frequencies of the geometry s. The corresponding vibrationally adiabatic transmission coefficient can be calculated, under the Wentzel–Kramers–Brillouin (WKB) approximation, as:
%kappa = { int_{0}^{%infinite}{P left( V_a right) e^{-{V_a over {k_B T} }} dV_a} } over { int_{V_a^max}^{%infinite}{ e^{-{V_a over {k_B T} }} dV_a} } ~~ approx ~~ e^{{V^max_a over {k_B T} }} 1 over {k_B T} int_{0}^{%infinite}{P left( V_a right) e^{-{V_a over {k_B T} }} dV_a}	(2)

where the approximation is valid at low temperatures[1]. Additionally, the recrossing factor can be also estimated:
[1] Equations 49, 50 from J.Phys.Chem. 1980 (84) 1730-1748
%gamma = e^{- { lline {%DELTA V^max_a - %DELTA V^{s=0}_a } rline over {k T} }}	(3)

being ∆V_a^{ s=0 } the barrier from the reactant to the transition state, and ∆V_a^max to the maximum of the adiabatic potential (the transition state may not be a maximum on the adiabatic potential...). The value of the tunneling probability for a given potential E is defined by[2]:
[2] Equations 44, 45 from J.Phys.Chem. 1992 (96) 5758-5772; or 1a from J.Am.Chem.Soc. 2002 (124) 3093-3124
P left( E right) = left( 1 + e^{2 cdot %theta left( E right)} right)^{ {}-1 } ~~~~ E <= V_a^{s=0} ~~~~~~~~ %theta left( E right) = {2 %pi} over h int_{ s<{} }^{ s>{} }{ left(2 %mu_eff (s)left[ V_a left( s right)- E right] right)^{1 over 2} ds }	(4)

where s< and s> are the values of the path coordinate at the left and right turning points, and %mu_eff( s ) is the effective reduced mass along s. If %mu_eff is taken constant along the reaction path, we obtain the Zero-curvature theory (ZCT). On the other hand, the centrifugal-dominant small-curvature tunneling approximation[3] allows to express the dependence of %mu_eff( s ) :
[3] Equations 52, 51, 50, 44 from Comput. Phys. Commun. 1992 (71) 235-262; and 3 from J.Am.Chem.Soc. 2002 (124) 3093-3124
%mu_eff(s) = %mu cdot min left lbrace e^{- 2 a(s) - left[ a(s) right]^2 + left( dt over ds right)^2 } ~,~ 1 right rbrace ~~~~~~ ~~~~~~ ~~~~~~ %mu = 1 over { N_A m_e 10^3 }	(5)

where a(s) and t(s) (the maximum concave-side vibrational displacement along the curvature direction) are:
a( s ) = t( s ) %eta( s ) ~~~~~~ t(s) = %eta^{ 1 over 2 }(s) left( h over {2 %pi %mu} right)^{ 1 over 2 } left[ sum from{i} to{3N-7}{ B_i^2(s) %omega_i^2(s)} right]^{ - {1 over 4} } ~~~~~~ %eta (s) = left( sum from{i} to{3N-7}{ B_i^2 (s) } right)^{ 1 over 2 }	(6)

being %eta( s ) the magnitude of the curvature, and B_i( s ) the reaction path curvature components:
B_i ( s ) = 1 over lline g(s) rline L^T_i(s) cdot { left[ H(s) cdot { {-g(s)} over lline g(s) rline } right] } ~~~~ ~~~~ %eta (s) = left( sum from{i} to{3N-7}{ B_i^2 (s) } right)^{ 1 over 2 }	(7)

In this expression, Li(s) corresponds to the ith eigenvector of the hessian H, and g is the gradient vector (all in mass-weight coordinates: x_i = sqrt{ m_i } x^cart_i ~~;~~ g_i = g^cart_i / sqrt{ m_i } ~~;~~ h_{ i,j } = h^cart_{ i,j } / sqrt{ m_i · m_j } ). Thus, the Bi(s) values represent the change in the direction of the ith eigenvector induced by the variation of the reaction coordinate.

For the particle in a box, the tunneling effect arises from the presence of a finite potential of the shape:
V( x ) left lbrace matrix { 0# x < 0# "region I"## U_o# 0 <= x <= L# "region II"## 0# x > L# "region III"} right none
The Schrödinger time-independent equation is solved for each region, thus obtaining three wave-functions, satisfying the continuity at each region, as well as in the first derivatives:
%psi_I( 0 ) = %psi_II( 0 ) ~~~~ ~~ %psi_II( L ) = %psi_III( L ) ~~~~ ~~ left none { d %psi_I(x) } over { dx } right rline_{ x=0 } = left none { d %psi_II(x) } over { dx } right rline_{ x=0 } ~~~~ ~~ left none { d %psi_II(x) } over { dx } right rline_{ x=L } = left none { d %psi_III(x) } over { dx } right rline_{ x=L }

The transmission coefficient represents the probability flux of the transmitted wave relative to that of the incident wave. Using the WKB approximation[4], one can obtain a tunneling coefficient that looks like (which depends on the particular system):
[4] See chapter 8 of “Introduction to Quantumn Mechanics” (ISBN: 0-13-191175-9)
T ={ e^{ -2 int_{x1}^{x2}{ sqrt{ {2 m} over { %Ux210F^2} left( V(x) -E right) } dx } } } over { left( 1 + 1 over 4 e^{ -2 int_{x1}^{x2}{ sqrt{ {2 m} over { %Ux210F^2} left( V(x) -E right) } dx } } right)^2 }
where x1, x2 are the two classical turning points for the potential barrier.

A description of the Variational Transition-State theory can be found at J.Phys.Chem. 1980 (84) 1730-1748

%theta left( x right) = s over { kg m^2 } int_{ s<{} }^{ s>{} }{ left( %mu right)^{1 over 2} sqrt{ 2 kg {m^2 over s^2 } } Å sqrt{ g over mol } } newline %theta left( x right) = left( s over { kg m^2 } int_{ s<{} }^{ s>{} }{ left( %mu right)^{1 over 2} sqrt{kg} {m^2 over s} sqrt{kg} } right) sqrt{2} {10^-10 over sqrt{10^3 · N_A} { {2 · %pi} over h } } newline newline a(s): "dimensionless" ~~;~~ t(s): s^{ -1 } ~~;~~ %eta(s): s ~~;~~ B_m(s): s